## Slide 1
EN(door up)-GPIO5
IN3(door_rotation)
IN4(door_rotation)
SCK
DT
VCC(24V)
GND
Load cell #2
A-
A+
E-
E+
SCK
DT
IN1(doorup)
IN2(doorup)
RX(pin7)
TX(pin6)
GND
VCC(5V)
VCC(24V)
Transformer
(24V-5v)
Switch Power supply
(24v, 14A)
Door Up&Down actuator
Door Rotation actuator
Hopper Actuator
IN1
EN
IN2
Load cell #1
A-
A+
E-
E+
GPIO9 - IN1, EN
EN(rood rot)-GPIO22

## Slide 3
Door Up&down
Door Rotation
Hopper

## Slide 4
0. Start
1. Door is at home position
2. Door is going up
3. Door is at the rotatable position
4. Door is rotating
5. Door is at opened position
6. Door is rotating reverse
7. Door is at the rotatable position
8. Door is going down
9. Door is at home position
10. Completed
Door open test
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
Hopper test
0. Start
1. Hopper is opening
2. Hopper is closing
3. Completed
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
OLED test
0. Start
1. Display #1
2. Display #2
3. Completed
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
Speaker test
0. Start
1. test #1
2. test #2
3. Completed
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
Temp
##
Humi
##
QR scanner test
0. Start
1. Scan QR code
2. Scanned and your QR is :
3. Completed
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
Hall effect sensor #1
Hall effect sensor #2
Hall effect sensor #3
Hall effect sensor #4
Cooling fan
0. Start
1. Fan #1 operation
2. Fan #2 operation
3. Completed
O.K / N.O
O.K / N.O
O.K / N.O
O.K / N.O
Load cell test
0. Start
1. Your weight is :
2. Completed
O.K / N.O
O.K / N.O
O.K / N.O
Tare
Calibration

## Slide 5
Door open test
Hopper test
OLED test
Speaker test
QR scanner test
Cooling fan
Load cell test
Main page

## Slide 6
Start
1. Door is at home position
(1. Please check hall effect sensor)
2. Door is going up – Please check actual operation
3. Door is at rotatable position
(3. Please check hall effect sensor)
4. Door is rotating – Please check actual operation
5. Door is at opened position
(5. Please check hall effect sensor)
6. Door is rotating reverse– Please check actual operation
7. Door is at rotatable position
(7. Please check hall effect sensor)
8. Door is going down – Please check actual operation
9. Door is at home position
(9. Please check hall effect sensor)
End
Home
If fail
Door open test

## Slide 7
Start
1. Hopper door opening – Please check actual operation
2. Hopper door closing– Please check actual operation
End
Home
Hopper test

## Slide 8
Start
1. Display #1 : AEL
2. Display #2 : ARCS inlet system
End
Home
OLED test

## Slide 9
Start
1. sound #1
2. sound #2
End
Home
Speaker test

## Slide 10
Start
1. Please scan your QR code
2. Scanned and your QR is
XXX
End
Home
QR code scanner
test

## Slide 11
Home
Temp, humi
and cooling
fan test
Temp
##
Humi
##
Cooling fan #1 test
Cooling fan #2 test

## Slide 12
Home
Load cell
test
Current weight output :
A/D value : 2031
Weight result : XXX kg
Next

## Slide 13
Home
Load cell
zero setting
Adjustment of zero point:
A/D value of left L/C : 2031
A/D value of right L/C : 3162
Avg of value : 2523
Current weight : xx kg
Click to zero setting
Adjustment of zero point:
A/D value of left L/C : 2031
A/D value of right L/C : 3162
Avg of value : 2523
Current weight : 0 kg

## Slide 14
Home
Load cell
Calibration 1
Put your standard weight
20kg
Next

## Slide 15
Home
Load cell
Calibration 2
Span adjust
20kg
L : 8504 R : 9684
Press ‘Next’ when both value get stable
Next

## Slide 16
Home
Load cell
Calibration 3
Weight display
20.00kg
Finish